## Slide 1
On-Off Keying Transceiver
RX
Frame Sync
CRC check
Controller
Memory
TX
Frame Prepare
CRC encoding
Analog
Frame stack
Frame send
OOKRX Block
OOKTX Block
Frame stack

## Slide 2
OOK Transceiver frame explanation
Assuming the frame is 32-bit long
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
| | | | |
Width: a b c d-1
W: Width of the whole frame (@frameWidth = 32)
a: Width of the frame bits (@frameBitsWidth = 8)
b: Width of the frame index (@frameIndexWidth = 4)
c: Width of the information data (@dataWidth = 16)
d: Width of divisor for CRC (@divisorWidth = 5). The LSB 4 bits are the CRC residue, so have d-1 width.
Relation: W = a + b + c + d - 1
Frame Bits
Frame Index
Information data
CRC residue
MSB
LSB

## Slide 3
Frame Sync
Frame Stack Rx
CRC Check
OOKRX Block (Chisel top-level code and tester)
requestFrame
Frame
W
FrameReady
Frame
W
requestFrame
FrameValid
divisor
d
c
dataOut
dataReady
CRCpass
bit
frameBits
a
Frame Sync: chisel code and tester
Frame Stack: chisel code and tester
CRC Check: chisel code and tester
RX
RxEn

## Slide 4
CRC Encode
Frame Stack Tx
divisor
d
bit
data
Frame Send
c
dataValid
requestData
requestFrame
requestFrame
frame
W
frameValid
frameBits
a
frameIndex
b
frame
W
frameValid
txEn
OOKTX Block (Chisel top-level code and tester)
CRC Encode: chisel code and tester
Frame Prepare: chisel code
Frame Stack: chisel code and tester
Frame Send: chisel code and tester
TX

## Slide 5
1-bit
b+c
dataTxValid
TxEn = 1
Top-level simulator Block (chisel code and tester)
“TopControl” block is here
“dataTx” is formed with Cat( frameIndex, data )
“dataRx” is formed with Cat( crcPassFlag, frameIndex, data )
Air
1-bit
dataTx
dataRx
1+b+c
dataRxReady
TX
RX
Tx enabled
TX
RX
Rx enabled
TopControl
TopControl